## Slide 1
Presentation Title ( Arial, Font size 28 )
Date, Venue, etc..( Arial, Font size 18 )
International Ferroalloys Conference
Tata Power Trading Company Ltd
07/09/2018
Power Procurement for Industrial Consumers
Regulation & Options

## Slide 2: Agenda
Introduction of Tata Power & Tata Power Trading Company Limited
Power Market Structure and Developments
Open Access and Barriers in OA
Group Captive
Power Market (ESCerts)
Power Market (DAM & TAM)
2

## Slide 3
Introduction of Tata Power &
Tata Power Trading Company Limited

## Slide 4
The Tata Power Company Limited
Business Overview
Established in 1910, Tata Power is India's largest integrated power company with a significant international presence
The Company has gross power generation capacity of 10857 MW out of which 7436 MW from Thermal.
Tata Power has an installed generation capacity of 3133 MW through green resources
One of the largest renewable energy players in India
It has developed India’s first 4000 MW Ultra Mega Power Project
Tata Power – International Presence
South Africa - Amakhala Emoyeni Wind Farm (134.4 MW) and Tsitsikamma Community Wind farm (95.325 MW)
Georgia - Development of two separate Hydro Power Projects of 185 MW and 150 MW
Indonesia – Coal Assets
Zambia - 120 MW Itezhi Tezhi Hydro Power Project (2 * 60 MW)
Bhutan – 126 MW Dagachhu Hydro Project (2 * 63 MW)
4

## Slide 5
Tata Power Trading Company Limited (TPTCL)
An Overview
A wholly owned subsidiary of The Tata Power Company Limited
First company to be awarded Category I Trading License by CERC
Cross Border Trading Experience – Importing power from Dagachhu Hydro Power (126 MW), in Bhutan, to India
Consistently among the top three power traders among a total of 33 Power Traders
Trading volume has increased from 4,354 MU in FY11 to 12,405 MUs in FY18 with highest of 17,305 MU in FY 2016
Trading volume has increased by CAGR of 16% between FY11 to FY18
Handled revenue of ₹ 3,707 Crore(s) during FY18 and ₹ 4,605 Crore(s) in FY17
State of art, highly automated control room being operated 24 X 7, by highly skilled professionals
Highly Efficient Receivable Management
Accredited with ISO:22301:2012 certification for Business Continuity Management System and with ISO 31000:2009 certification for Risk Management
Strong presence in all states of India and cross border energy trade
5

## Slide 6
Tata Power Trading Company Limited (TPTCL)
Service Portfolio
TPTCL SERVICE PORTFOLIO
Bilateral Power Contracts
Short Term Contracts
Medium/Long Term Contracts
Power Exchanges
Renewable Energy Certificate (REC)
Advisory Services
Group Captive
Captive Wheeling of Power
Banking
Qualified Coordinating Agency
Energy Saving Certificates (ESCerts)
6

## Slide 7
Power Market Structure and Developments

## Slide 8: Salient Features Of Indian Electricity Act 2003
8
De-licensing of generation
Development of a Multi-Buyer Multi-Seller framework in power
Introduced Tariff based Competitive Bidding for procurement of Power
Provision of Non-discriminatory Open Access
Setting up State Electricity Regulatory Commission (SERC) made mandatory
Development of National Electricity Policy (NEP-2005) and National Tariff Policy (NTP-2016)

## Slide 9: Structure Of Indian Power Market
REGULATORS
SYSTEM OPERATORS
GENERATION
POLICY MAKING
CENTRAL GOVERNMENT
STATE GOVERNMENTS
CENTRAL ELECTRICITY REGULATORY COMMISSION
STATE ELECTRICITY REGULATORY COMMISSIONS
NATIONAL LOAD DISPATCH CENTER
STATE LOAD DISPATCH CENTERS
CENTRAL GENERATING STATIONS
PRIVATE SECTOR PLAYERS
TRANSMISSION
STATE GENERATING STATIONS
CENTRAL TRANSMISSION UTILITY
PRIVATE SECTOR PLAYERS
STATE TRANSMISSION UTILITIES
REGIONAL LOAD DISPATCH CENTERS
DISTRIBUTION
PRIVATE SECTOR DISTRIBUTION LICENSEE
MARKETS
STATE SECTOR DISTRIBUTION LICENSEE
TRADING LICENSEE
BILATERAL MARKETS
RENEWABLE ENERGY
RENEWABLE ENERGY CERTIFICATES
RENEWABLE PURCHASE OBLIGATION
ENERGY EFFICIENCY
ENERGY SAVING CERTIFICATES (ESCERTS)
ENERGY EFFICIENCY TARGETS
CEA
POWER EXCHANGES
9

## Slide 10: Installed Generation Capacity
Source: Central Electricity Authority
As on 30.06.2018 | Thermal (MW) |  |  |  | Nuclear (MW) | Hydro (MW) | RES (MW) | Grand Total (MW)
 | Coal (MW) | Gas (MW) | Diesel (MW) | Total (MW) |  |  |  | 
State | 64456 | 7079 | 364 | 71899 | 0 | 29858 | 2003 | 103760
Private | 75546 | 10580 | 474 | 86600 | 0 | 3394 | 65517 | 155511
Central | 56955 | 7238 | 0 | 64193 | 6780 | 12151 | 1502 | 84626
Total | 196957 | 24897 | 838 | 222692 | 6780 | 45403 | 69022 | 343897
RES as on 31.03.2018 |  |  |  |  |  |  |  | 
Chart: Generation Mix
| Thermal | Nuclear | Hydro | RES
 | 222906.59 | 6780 | 45293.42 | 69022.391
Chart: Sector-Wise Generation
| State | Private | Central
 | 103974.75 | 155511.021 | 84516.63
10

## Slide 11: Generation Mix (MW)
Source: Central Electricity Authority
Chart: Generation Mix as on 31.03.2010
| Thermal | Nuclear | Hydro | RES
 | 102453.98 | 4560 | 36863.4 | 15521.11
Installed Hydro capacity has been fallen from 23% in FY10 to 13% in FY18
Renewable Generation has increased from 10% in FY10 to 20% in FY18
Increase in Renewable Power generation is mainly from Solar Power and Wind Power
Chart: Generation Mix as 31.03.2018
| Thermal | Nuclear | Hydro | RES
 | 222906.59 | 6780 | 45293.42 | 69022.391
11

## Slide 12
Power Supply Position In India
Source: CEA
Power Supply Position in the country during FY10 to FY18 |  |  |  |  |  |  |  | 
 | Energy |  |  |  | Peak |  |  | 
Financial Year | Requirement (MUs) | Availability (MUs) | Deficits (MUs) | Deficits (%) | Peak Demand (MW) | Peak Met (MW) | Deficits (MW) | Deficits (%)
2010-11 | 861,591 | 788,355 | 73,236 | 8.5 | 122,287 | 110,256 | 12,031 | 9.8
2011-12 | 937,199 | 857,886 | 79,313 | 8.5 | 130,006 | 116,191 | 13,815 | 10.6
2012-13 | 998,114 | 911,209 | 86,905 | 8.7 | 135,453 | 123,294 | 12,159 | 9.0
2013-14 | 1,002,045 | 959,614 | 42,431 | 4.2 | 135,918 | 129,815 | 6,103 | 4.5
2014-15 | 1,068,943 | 1,030,800 | 38,143 | 3.6 | 148,166 | 141,160 | 7,006 | 4.7
2015-16 | 11,14,235 | 10,90,713 | 23,522 | 2.1 | 153,366 | 148,463 | 4,903 | 3.2
2016-17 | 11,42,092 | 11,34,631 | 7,461 | 0.7 | 159,542 | 156,934 | 2,608 | 1.6
2017-18 | 1,212,134 | 1,203,567 | 8,567 | 0.7 | 164,066 | 160,752 | 3,314 | 2.0
Chart: Deficit in Energy - MUs/(%)
| 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 | 2014-15 | 2015-16 | 2016-17 | 2017-18
Deficits (MUs) | 83950 | 73236 | 79313 | 86905 | 42431 | 38143 | 23522 | 7461 | 8567
Deficits (%) | 10.1 | 8.5 | 8.5 | 8.7 | 4.2 | 3.6 | 2.1 | 0.7 | 0.7
Chart: Deficit in Peak - (MW)/(%)
| 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 | 2014-15 | 2015-16 | 2016-17 | 2017-18
Deficits (MW) | 15157 | 12031 | 13815 | 12159 | 6103 | 7006 | 4903 | 2608 | 3314
Deficits (%) | 12.7 | 9.8 | 10.6 | 9 | 4.5 | 4.7 | 3.2 | 1.6 | 2
12

## Slide 13: Indian Power Market Structure Types of Power Procurement Contracts
Source: CEA
13
Nature of Contract | Duration of Contract | Transmission Open access availability
Long Term | >7 years & Upto 25 Years | Long term open access is available for a period more than 7 years
Medium Term | >1 Year & Upto 5 years | Medium term open access is available for a period of 3 months to 5 years
Short Term |  | 
Short Term – Bilateral | Up to 1 year | For a period of up to 3 months
Short Term – Power Exchange | Day Ahead Market (1 day) | 1 day (corridor left after short term bilateral)
 | Term Ahead Market ( Week Ahead) | Weekly basis (FCFS/Day Ahead)
Deviation Settlement Mechanism | Real time balancing mechanism for settling deviation from schedule | 

## Slide 14
Transmission Corridor Priority
Long
Term
Medium Term
Short Term
(Advanced Reservation /First Come First Serve)
Short Term PX(DAM)
Short Term Day Ahead / Contingency / Same day
Procurers must keep in mind the priority for transmission corridor related to various options available for power procurement.
14

## Slide 15
Indian Power Market – Percentage Energy Share
Largely tied-up through Long term PPAs
Short term bilateral market dominated by few players accounting for over 85% volume of short term market
Low liquidity in short term market
Coal India Limited (CIL) giving coal only for long term PPAs
Volume settled through DSM is progressively declining because of tightening of frequency band by Central Electricity Regulatory Commission) CERC and emergence of Power Exchange (PX)
Chart: Percentage Energy Share Contract Wise
| Long Term | Short Term- OTC | Short Term- PX | Short Term- DSM
 | 0.9 | 0.05 | 0.03 | 0.02
15

## Slide 16
Open Access & Barriers

## Slide 17
17
The Electricity Act 2003 introduced Open Access, to create market driven power procurement as opposed to supply of electricity through state monopolies
“open access” means the non-discriminatory provision for the use of transmission lines or distribution system or associated facilities with such lines or system by any licensee or consumer
A consumer consuming more than 1 MW is eligible to choose their supply source on payment of open access charges from one or more:
  Trading Licensee
  Power Exchange
  Generating Station including Captive Generating Plant
  Other Distribution Licensees
State Regulators (SERC) decide the eligibility conditions of the Open access and various charges associated with it
Reliability of supply and Competitive rates are the two primary reasons that drive procurement through open access route
Power Procurement Through Open Access (1/2)

## Slide 18
Power Exchange
Bilateral
  Interstate
  Intrastate
Captive
Group Captive
Any Other Distribution Utility
Power Procurement Through Open Access (2/2)

## Slide 19: TPTCL Presence in Open Access
TPTCL Open Access Customers –
  Industries/Continuous process
  Hotels/Commercial complexes
  SEZs/IT parks
TPTCL has contracted 300+ industrial clients in bilateral and power exchange and has supplied more than 1000 Million Units in FY18 to open access consumers
Active Consumers with TPTCL is in excess of 600 MW
Cross Border sale of power to OA Consumers
TPTCL Renewable Focus
Supplied power from Small Hydro, Solar, Wind, Biomass, Bagasse to OA Consumers

## Slide 20: Barriers for Open Access
Barriers in Open Access:
Cross Subsidy Surcharge
Stranded Capacity Surcharge
Regulatory Asset charges
Subsidy given in backward areas
Lapsed Units
Standby Power
Conditional NOC
Technical criteria imposed by DISCOM
Denial of Open Access
Removal of benefits provided to renewable sources
Applicability of CSS on captive consumers in some cases

## Slide 21
Power Exchange – DAM

## Slide 22: Features Of Day Ahead Market Of Power Exchange
A closed double-sided anonymous auction for each 15-min time block for the following day
The intersection between the aggregated sale and purchase curves defines the market clearing price (MCP)
13 Bid area defined
Congestion Management through market splitting and determining Area Clearing Price (ACP) specific to an area
Bid types: Portfolio Orders or Block Orders
Minimum bid=Re.1 for 0.1MWh
Minimum Price & Volume Step = 0.1p * 0.1 MWh
N1
N2
A2
A1
W3
E2
E1
N3
W2
W1
N2
S2
S1
Source – IEX
S3
22

## Slide 23: Timeline- Day Ahead Market
N1
N2
A2
A1
W3
E2
E1
N3
W2
W1
N2
S2
S1
Source – IEX
IEX BID AREAS
D-1 (one day before delivery) | 
Time (IST) | Activities
9:30 Hrs | Initial Margin Check
10:00-12:00 Hrs | Bid-Call Session
 | - Double sided closed bidding
 | - Member can submit, edit, modify or delete buy and sell bids
12:00-13:00 Hrs | Exchange calculates MCP and provisional obligation of the members
 | Communication of unconstrained solution to National Load Despatch Centre (NLDC)
 | Communication to bank to confirm and block the funds for pay-in from buyer member's settlement account
13:00-14:00 Hrs | NLDC checks for transmission availability on ISTS. In case of congestion, NLDC intimates the period for congestion and available margins
By 14:30 Hrs | Buyers pay to IEX (Pay-in)
By 15:00 Hrs | IEX calculates ACP based on transmission network availability and sends 'scheduling request to NLDC
By 17:30 Hrs | NLDC confirms acceptance. IEX sends detailed scheduled to SLDCs
By 18:00 Hrs | RLDCs/SLDCs incorporate collective transactions in the daily schedule
D+1 (one day after delivery) | 
Time (IST) | Activities
By 14:00 Hrs | IEX makes payment to seller (Pay-Outs)
S3
23

## Slide 24: Model Price Calculation Algorithm
Source – IEX
0 | 1 | 1.1 | 2 | 2.1 | 2.5 | 3 | 3.1 | 4 | 4.1 | 5 | --- | --- | ---- | 20
20 | 20 | 20 | 20 | 20 | 20 | 20 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0
60 | 60 | 60 | 60 | 50 | 40 | 40 | 40 | 40 | 40 | 20 | 20 | 20 | 20 | 20
40 | 20 | 0 | 0 | -40 | -60 | -80 | -81 | -120 | -120 | -120 | -120 | -120 | -120 | -120
120 | 100 | 80 | 80 | 70 | 60 | 60 | 50 | 40 | 40 | 20 | 20 | 20 | 20 | 20
0 | 0 | 0 | 0 | -40 | -60 | -80 | -81 | -120 | -120 | -120 | -120 | -120 | -120 | -120
120 | 100 | 80 | 80 | 20 | 0 | -20 | -21 | -80 | -100 | -100 | -100 | -100 | -100 | -100
Price Tick (Rs.)
Portfolio A, MW
Bid Quantum by different portfolios
Total Sell Quantum received, MW
Total Buy Quantum received, MW
Net Transaction, MW
Portfolio B, MW
Portfolio C, MW
Price
MW
Market clearing
price (MCP)
Market Clearing Volume (MCV)
Supply
(Sell)
Demand
(Buy)
Volume
2.5
60
24

## Slide 25: Trend of Market Clearing Price in IEX (₹/KwH)
Source: IEX Website
Chart: 
| FY10 | FY11 | FY12 | FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19 till Aug'18
MCP(₹/KwH) | 5.187 | 3.564 | 3.536 | 3.487 | 2.801 | 3.511 | 2.731 | 2.414 | 3.255 | 3.815

## Slide 26
Power Exchange – ESCerts

## Slide 27: Energy Saving Certificates (Escerts)- PAT Scheme
MOVING TOWARDS ENERGY SAVING
National Action Plan on Climate change (NAPCC) introduced National Mission for Enhanced Energy Efficiency (NMEEE)
The National Mission for Enhanced Energy Efficiency proposed an Energy Efficiency Action Plan which comprises of 3 aspects.
PERFORM:
ACHIEVE:
TRADE:
PAT is a market based mechanism - Reward for over achiever & Penalty for under performer
PAT cycle:
Setting the Targets
Monitoring & Verification
Trading of ESCerts
27

## Slide 28: Concept Of Target, Compliance, ESCerts & Penalty
Target
Achieved SEC
Scenario 2
Scenario 1
Compliance
Target SEC
Purchase Escerts
Issued Escerts Penalty
Baseline SEC
Purchase ESCerts
When a designated consumer (DC) achieve and surpass the targets, ESCerts are to be issued by MoP and the same can be sold to DC who fail to achieve their targets so as to comply energy consumption norms and standards
One ESCert = One Tonne of Oil Equivalent = 11.63 MWh

## Slide 29
`
Key Features – ESCerts Transactions
Sellers – ESCerts issued to Designed Consumers (DC)
Buyer – DCs who under achieved the targets obligated to purchase ESCerts
ESCerts once purchase can not be resold.
DCs may use balance ESCerts after the compliance in first cycle , if any, and such banked ESCerts may be used for the compliance of their next cycle or sold.
Validity for ESCerts - till the completion of the compliance period of respective DC’s next cycle.
As per procedure, registration has to be done with in 30 working days with Registry.
After registration with Registry, the DCs to register with Power exchanges, for trading.
Trading of ESCerts shall be done through closed double sided uniform price auction.
Bilateral trading even within the same corporate group not permitted
29
Notes: 29

## Slide 30
`
ESCerts Trading Under PAT Scheme
PAT cycle I – April 2012 to March 2015
Target – Reduction of 6.686 million tonnes of oil equivalent (mtoe)
Designated Consumers – 478 entities in total 8 Sectors
PAT Cycle II – April 2016 to March 2018
Target – Reduction of 8.869 million tonnes of oil equivalent (mtoe)
Designated Consumers – 621 entities in total 11 Sectors
PAT deepening/widening – Railways, DISOCMs & Refinery covered
Trading of ESCerts under PAT cycle I
Total 38 lakhs ESCerts issued and total 14.25 lakhs ESCerts were to be purchased.
Out of total 14.25 lakhs ESCerts purchase (as a compliance), 12.98 lakhs ESCerts were purchased by DCs on Average Discovered prices Rs 619 per ESCert.
TPTCL Traded total 1.76 lakhs ESCerts with 10% market share
Major clients were UP Thermal Power Station Harduaganj, Rajasthan Barmer Thermal Station, SAIL Bokaro, Tata Steel
30
Notes: 30

## Slide 31
Group Captive

## Slide 32
Power Procurement- Consumers (Group Captive)
Captive Consumers can be:
  Association of Persons or a Co-operative Society: Such captive user(s) shall hold at least 26% of the ownership in the generating plant and consume not less than 51% of the electricity generated, on an annual basis, in proportion to their shares in ownership of the power plant within a variation not exceeding ten percent
Advantages
  Avoidance of Cross Subsidy Charges
  Minimal intervention of the area distribution company
  Typical Attributes of GCPP Route of Power Procurement
  Share Capital per MW ranges anywhere between Rs. 40,000 to Rs.56 Lakh, based on equity structure
  Involves Fuel Risk
  2 to 5 years of contract period
  The power prices is sensitive to the quantum contracted
  Monthly Billing
  Involve Lock In period
  RPO to be separately met by participating entities
  100 % scheduling for allotted capacity
32

## Slide 33
GCPP Structure
Association of Persons (for example SPVs)
S. No. | Captive consumer | Ownership (%) | Consumption (%) | Variation allowed (%) | Allowed Consumption (%)
1 | 1 | 6% | 12% | +/- 10% of 12% | Within 10.8% - 13.2%
2 | 2 | 10% | 20% | +/- 10% of 20% | Within 18% - 22%
3 | 3 | 8% | 16% | +/- 10% of 16% | Within 14.4% - 17.6%
4 | 4 | 2% | 4% | +/- 10% of 4% | Within 3.6% - 4.4%
 |  | 26% | 51% | 51% | Equal to or more than 51%
Each captive user retains its own individual identity as consumer of power.
GCPP feasible with only one captive user provided it complies with the ownership and consumption requirements specified.
Association of Persons (in various forms like SPVs) formed with more than one captive user for the generating plant.
Promoter
Captive consumer 1
Captive consumer 2
Captive consumer 3
Captive consumer 4
Generating Plant
74%
6%
10%
8%
2%
33

## Slide 34
Key Risks_ (Group Captive)
S. No. | Key Risks | Mitigation Mechanism
1 | Compliance with respect to minimum equity. Requirement: Captive consumers to have at least 26% of the ownership in the generating plant. | Ensuring that the ownership stake held by captive consumers is higher than this threshold requirement by at least 3 – 4%.
2 | Compliance with respect to minimum consumption Requirement: At least 51% of the electricity generated from the generating plant, determined on annual basis, in proportion to their shares in ownership of the power plant within a variation not exceeding ten percent (10%). | PPA to have provisions wherein captive consumers shall provide quarterly consumption forecasts and the captive generator will monitor compliance to these forecasts on monthly basis. Any deviation noticed will have corrective actions. Should there be genuine issues on consumption, steps will be taken to align the ownership status appropriately through equity purchase/sale among captive consumers. Share Holder Agreements to have appropriate mechanisms in place.
34